## Slide 1: PACEdge 3.0.0 Technical Training
April 2026

## Slide 2: PACEdge 3.0.0- Technical Training Agenda
 | Introduction to the PACEdge Platform
 | PACEdge Architecture Overview
 | PACEdge Product Offerings
 | PACEdge Getting Started
Notes: Changing the color bars in the agenda table works the same as changing them in the side bar tables.
Click in the space to the right (or left) of the bar
Then go to the Design tab under the Table Tools
Change your Pen Weight to be 6pt
Select the color you would like to change it to
Then click the down arrow under Borders and select right or left border (depending on which side you clicked in originally…)

## Slide 3
PACEdge is an IIoT Application Enablement Platform for the development of scalable data intensive Industry 4.0 solutions requiring integration between the OT and IT domains without disrupting OT assets, architectures or systems while satisfying IT cybersecurity, communications and application requirements.
Notes: To replace the photo:
Select the transparent gradient overlay right click, choose Arrange > Send to Back
Select the photo and press delete on your keyboard
From the Insert menu, choose Insert Photo > Picture from File
Crop and resize photo to fill slide (hold down Shift key while resizing to maintain picture aspect ratio)
Select the photo, right click, choose Arrange > Send to Back so the photo is behind the gradient
To edit text:
Click inside a text box, scroll over (with your mouse) to select all text and begin typing

## Slide 4: PACEdge and Movicon Software Suites
FIELD / MACHINE LEVEL
CLOUD / ENTERPRISE LEVEL
RX3i CPL4XX Edge Control
Edge &
Computing
Supervisory
Layer
PLANT LEVEL
MOVICON
HMI/SCADA
MOVICON PRO.LEAN / PRO.ENERGY
Data Aggregation, Analytics, Visualization, Modeling
PACEdge
Notes: Resolution: Introducing PACSystems Edge Solutions

## Slide 5: PACEdge Supports The Unique Needs Of Use Cases and Applications That Lie At The Intersection Of OT & IT Systems
PACEdge
At The Intersection of OT & IT Lie Features And Functionality Unique To Use Cases And Applications Such As AI/ML Execution For Quality Analysis, Edge-to-Enterprise Processing For Energy Management And Remote Monitoring For Equipment Maintenance
Controllers
SCADA
Sensors
Machines
Robotics
Historians
HMI
Cloud
Enterprise
Servers
Data Lake
Analytics
AI/ML Model
OT Protocols
Processing & Analytics
Visualization
Contextualization
IT Integration
Cybersecurity
AI/ML Execution
OT Systems
IT Systems
Industrial PC
Notes: To edit text:
Click inside a text box, scroll over (with your mouse) to select all text and begin typing
To remove primary information tabs:
Select and delete unwanted tabs – recommend starting at the bottom
To add primary information tabs:
Select and group all existing tabs
Resize the group to create space for additional tabs and ungroup
Select the bottom tab and CTRL-Shift-Drag to make an aligned copy (or copies)
Distribute the tabs using the Arrange button on the Home tab and the Distribute command

## Slide 6: The Value Of PACEdge Is In It’s Powerful Easy-to-Use Development Environment Supported Throughout The Life Of The Application
Easy-to-Use
Powerful
Supported
Graphical Development Environment
Intuitive User Interface
Built-In Tooling & Platform Services
Modern Data & Machine Visualization
Communicates With 30+ Protocols
On-board Data Storage & Processing
AI/ML execution environment
Fully Integrated & Validated Releases
Timely Security & Defect Resolution
Continuously Enhanced Features
Notes: To replace the icons:
Select an icon to use from the back of this deck or another source and copy it to the slide
Size the replacement icon to match the existing icon
Select the original icon, right click, choose Arrange > Bring to Front so the old icon is in front
Align the new icon to the existing icon using the Arrange button on the Home tab and the Align or Distribute commands
Delete the original icon
To edit text:
Click inside a text box, scroll over (with your mouse) to select all text and begin typing
To remove an icon and primary/secondary information text set:
Select a set and delete
Group each remaining set and arrange on the slide using the Arrange button on the Home tab and the Align and Distribute commands
To add an icon and primary/secondary information text set:
Resize the elements to make room if required
Group each set
Select a set and CTRL-Shift-Drag to make an aligned copy
Adjust the color of the new copy
Arrange the grouped sets on the slide using the Arrange button on the Home tab and the Align and Distribute commands

## Slide 7: PACEdge Technical Architecture
PACEdge Technical Architecture

## Slide 8: PACEdge 3.0.0 Platform Components
8
Optimizing Edge-to-Cloud Controls
OPEN interoperable Edge intelligence
Application Enablement Platform
APPS
Linux server
Mqtt broker
I/O DATA SERVER
Cockpit
WEBHMI & GRAFANA
MYSQL & INFLUXDB
APPS
NODE-RED
CONNEXT & MOSQUITTO
HMI & DASHBOARD
LOGIC &
FLOW CONTROL
APPS
DATA
STORAGE
IT/OT DEVICE
INTEGRATION
PORTAINER.io
APPS
App Management
Group Manager
pgAdmin
MQTT Explorer

## Slide 9: PACEdge is a Platform
Set of pre-integrated software tools, geared towards: Data logic, analytics, communication, database, visualization
Browser Based Graphical User Interface
Based on standard Linux Server 24.04
HW independent (runs on x86, ARM, VMs)
Typical use case: Headless PACEdge device, controlled from any PC with web browser or remote ssh session for configuration and debug

## Slide 10: PACEdge is based on Docker Containers
Docker Container is just a “process” running in Linux
Containers reuse same Linux Kernel, but each has its own File System, binaries, libraries
Containers are isolated from each other and from the host OS !!
Containers are much lighter weight than Virtual Machines are, hence less memory, less storage, faster to come up and to shutdown
Communication Container-Container, Container-Host is via network interfaces (REST API, MQTT, etc)
Docker Containers v.s. Virtual Machines

## Slide 11: PACEdge Cyber Security
Applications are segregated from each other using Containers
Most network ports are closed for security reasons
Specific applications (Node-RED, Grafana, Connext, WebHMI, Portainer) are accessed via Traefik (proxy)
Internal network between containers is not accessible from the outside
Two instances of MQTT Broker:
  Internal: container to container communication
  External: open port for external communication
External communications encrypted using TLS
UEFI firmware protected via Secure Flash and supports Secure Boot technology
User roles, each with different privileges and password
Public Key Infrastructure (PKI) utility integrated into PACEdge
Cyber security penetration tested by an external security team
More details in the PACEdge Secure Deployment Guide

## Slide 12
Node-RED: PACEdge Logic Engine
Node-RED application where main logic and control happens:
  Send/Receive data:
    MQTT
    OPC-UA
    Modbus TCP
    HTTP
    TCP/UDP
    Email
  Database In/Out:
    InfluxDB (time series database)
    Timescale (relational & time series database)
  Logic, Analytics, Math
  Dashboard for visualization
  Tons of 3rd party nodes
For introduction on how to use Nod-RED please use following resources:
  PACEdge Node-RED Basics video at PACEdge Knowledgebase and Examples SFDC site
  Use extensive on-line resources, for instance: https://nodered.org/docs/tutorials/
Nodes (functions)
Main Design Window
Debug Messages

## Slide 13: Grafana: Data Visulization, Analytics, Dashboarding
Grafana:
Browse and Visualize time series data
Perform database queries and data analytics
Create sophisticated dashboards
For more details: InfluxDB and Grafana Basics at PACEdge Knowledgebase and Examples SFDC site

## Slide 14
Connext and WebHMI
Connext:
support for 2+ field busses
production grade OPC-UA Server
ideal for data gateway
WebHMI:
leading edge graphics

## Slide 15
Connext and WebHMI Deployment Model
More information: Connext examples and videos at PACEdge Knowledgebase and Examples SFDC site
Movicon.NExT
Windows PC
PACEdge IPC
Develop Connext or WebHMI Project
Deploy to PACEdge
Add, if required, Node-RED, Grafana, other components
I/O Data Server
OPC UA Server
WebHMI
Timescale
Node RED
Grafana

## Slide 16: Jupyter - Python
Jupyter - Python:
Jupyter is a graphical interface into Python programming
Python is ideally suited for the AI and ML model execution
IPC6010/7010/8010 has a strong built-in GPU that can be used to accelerate model execution
Tested models include Yolo Object Detection models and up to 8B parameter LLM models

## Slide 17
Portainer: Docker Container Management Tool
For more details: PACEdge Docker Container Management (at PACEdge Knowledgebase & Examples SFDC site)

## Slide 18: Data Communication Model: Southbound - Northbound data flow
From data flow perspective, data is:
being gathered from sensors, PLCs and other field devices (Southbound)
Processed, stored
visualized via dashboards and WebHMI on the Edge unit
sent out to Enterprise, SCADA, Cloud (Northbound)

## Slide 19: PACEdge: Platform with Many Options
From data flow perspective, Data:
Is being gathered from sensors, PLCs and other field devices (Southbound)
  Requires variety of field busses and protocols, some proprietary to specific vendors
  Connext is well positioned for this connectivity
Is Processed and Stored
  Node RED, Python, Telegraf, databases
Is visualized via dashboards and WebHMI on the Edge unit
  WebHMI, Grafana, Node RED Dashboard
Is sent out to Enterprise, SCADA, Cloud (Northbound)
  OPC UA Server, MQTT, Cloud connectors
  Connext, Node RED and Telegraf play a role here

## Slide 20: Use Case: a simple Gateway
Customer Requirements:
Get data from different Controllers and Sensors, connect data islands
Publish consolidated data via OPC UA Server
PACEdge implementation:
Use Connext to gather data
  Use many proprietary Drivers in Connext
  If needed, create a custom Driver in Connext
Use OPC UA Server in Connext to share consolidated data

## Slide 21: Use Case: a Gateway with Data Processing and Analytics
Customer Requirements:
Get data from Controllers and Sensors, connect data islands
Manipulate Data (filter, consolidate, calculations, logic)
Visualize and Analyze historical data, create dashboards and data views on the fly
PACEdge implementation:
Use Node-RED to gather data
  High volume of data storage to InfluxDB/TimeScale
Use Node-RED for data manipulation, processing, mathematics, store results in InfluxDB/TimeScale
Use Grafana to visualize and analyze the data in a very flexible way
(option) Use OPC UA Server to share consolidated data
(option) Send data to AWS, Azure, InfluxDB clouds through built-in cloud connectors in Node-RED

## Slide 22: Use Case: WebHMI
Customer Requirements:
Get data from Controllers and Sensors
Visualize data via WebHMI
PACEdge implementation:
Use Connext to gather data
  Use existing Drivers in Connext
  Create a custom Driver in Connext
Use WebHMI to visualize data
(option) Use OPC UA Server to share consolidated data

## Slide 23: Use Case: Quality Prediction using Machine Learning
Customer Requirements:
Get data from Controllers and Sensors
Process data using Machine Learning algorithm
Store results in Database
Visualize Results and Analyze historical data
PACEdge implementation:
Use Node-RED to gather and pre-process data
  High volume of data storage to InfluxDB
  Data pre-processing
  Send data to Machine Learning engine, perhaps running in custom Python container
  Store results in InfluxDB
Use Grafana/Node-RED Dashboards to visualize results and implement data entry functions
Use MQTT and Cloud connectors to share data
(option) Use WebHMI
(option) Use OPC UA Server to share consolidated data

## Slide 24: Real Use Case in Augsburg manufacturing: PACEdge with Object Detection Application
Connectors (through-hole, 576-pins total)
Analysis Results
Camera
Use Emerson Products to improve our own manufacturing process
Concept:
Use camera to take a picture of connectors
Use custom trained Object Detection Model to distinguish each connector hole and detect if pin is present or not
NOTE: ML model runs on the built-in GPU using OpenVINO framework, accelerating inference by at least 10x and freeing up CPU for other tasks.
Store results in the database
Data Acquisition
AI Inference and analysis
Result Storage

## Slide 25: PACEdge with Object Detection Application: Details
Emerson Monitor
Board under Test
Camera
IP Cammera
Python:
Object Detection Model with GPU acceleration
Node-RED:
Communication, logic
TimescaleDB:
Store Results
PACEdge Platform
Rollable Cart
MQTT
New 6010/7010/8010 IPC
Node-RED Dashboard:
User Interface

## Slide 26: PACEdge Product Offerings
PACEdge Product Offerings

## Slide 27: Tiered Software Offerings
+ Group Manager (10, 50, 100 managed devices)
Group
Manager
FUNCTIONAL TIERS
TARGET APPLICATION / USE CASES
PACEdge platform, including Open Standard communication protocols, data storage, analytics and visualization
+ WebHMI Visualization and Connext

## Slide 28: HW Options
2010 IPC
6010/7010/8010 IPC
Edge Core
Edge Core
Edge Core
Edge Core
Connext
Web HMI
Controller
Controller
CPE400
CPL410
Web HMI
Connext
Connext
6010/7010/8010 IPCkey specs:
  5x-20x x86 CPU cores at up to 5Ghz
  4GB-64GB RAM
  5x 2.5Gigabit Ethernet
  Up to 4 Displays
2010 IPC key specs:
  2x-4x ARM A53 cores at 1.2GHz
  2-4GByte RAM
  64GB SSD
  2x Gigabit Ethernet
  Optional WiFi/Cellular Module (add-on)
New Levels of Performance IPC
2010 IPC
6010/7010/8010 IPC

## Slide 29: PACEdge Getting Started
PACEdge Product Offerings

## Slide 30
WEB Interface: Getting Started
Two Setup Cases: Headless (most common) and Direct (not available for CPE400/CPL410)
Direct Use Case:
  attach Monitor, keyboard, mouse directly to the PACEdge device. Note: IPC2010 requires Emerson special USB-C to DP cable
  log-in using user: admin and default password: edgestack, change Linux password as requested
  open Firefox browser and enter address: localhost
Headless Setup (using static IP address):
  Via Ethernet, connect your PC to PACEdge ethernet port (consult Quick Start Guide or User Manual for details)
  Configure your PC IP address to be on the 192.168.3.x subnet
  On your PC open any web browser, enter IP address: 192.168.3.100
  First, you will get a warning that device is using a self signed certificate. Click on Advanced and then on Accept and Continue.
  log-in using user: admin and default password: edgestack, change Linux password as requested
For details please consult: Quick Start Guide for your specific hardware and Getting Started PACEdge v3.0.0 video

## Slide 31
WEB Interface: Getting Started
Read through the EULA and accept its conditions
Next, you will be guided to the service selection and password management page
In PACEdge v3.0.0 certain services, such as reverse proxy, Node-RED and Grafana, are mandatory, where is other services such as Python, external MQTT broker, management tools, are optional. When first time setting up the PACEdge device user gets to choose what optional services should be enabled
Note: each enabled service will consume CPU and memory. Movicon and Python are especially resource hungry. On the weaker hardware (CPE/CPL and IPC2010, enable only the minimum required services)
Note: there are two independent sets of passwords: Linux/Cockpit and PACEdge Services. Linux/Cockpit password was changed during the first login step, where is PACEdge application and services password needs to be set in this page.
PACEdge defines four user roles and a Movicon project deploy credentials
  admin
  developer
  service
  operators
Each role has different privileges and its own password
Once services have been selected and required passwords entered, click on Configure Device button.
Note: Configure Device task is extensive and will take some time to complete. On slower hardware (CPE400) up to 19 minutes.
Once services are enabled and passwords are set, PACEdge will allow user to navigate around and start developing applications
PACEdge Application and Services selection and their password Management

## Slide 32
Cockpit: PACEdge Management and Development Environment
New in PACEdge v3.0.0: during the initial login, based on the user role, it is redirected to either a developer environment or operators environment (clean page in kiosk mode with selected shortcuts)
Developers environment (Cockpit based) will have a tab bar on the left side, where
  upper portion (System) has OS and device configuration tools:
    IP addresses
    storage
    file manager
    service configuration and password management
    software updates
    licensing
  lower portion (Tools) has links to the PACEdge applications and services:
    Node-RED
    Grafana
    WebHMI
    Jupyter-Python
    Portainer
    Database managers

## Slide 33: Setting IP Address
Settings->Networking tab allows user to set IP addresses
To change the settings user needs to have Administrative access rights (upper right corner of the window)
Note: user can not modify IP address which is being used for current connection

## Slide 34: Enabling Additional User Accounts
Settings->Accounts tab allows admin user to set/change Linux user passwords and to enable additional user accounts:
  developer
  service
  operators (note the “s” at the end)
developer and service accounts are pre-configured and only require a valid password to be set
operators account can be easily created by clicking on the Create new account button and entering name and password

## Slide 35: Monitoring Storage
Settings->Storage tab allows admin user to monitor storage usage
It also allows user to mount USB stick, so that it can be accessed by the services and applications

## Slide 36: Updating PACEdge Software
There are 3 ways software can be updated:
  Single Internet connected device: pulls the update files from the on-line repository
  Single air-gapped device: user downloads update files and puts them onto the PACEdge device, via USB stick or local network
  Multiple devices can be updated via Group Manager
System Administration tab allows admin user to update Linux OS and PACEdge applications and services, note System and Services tabs at the top
It also allows user to choose between on-line repository and on device files
For software upgrades via Group Manager refer to the dedicated how to guides and Users Manual.
Note: image shows downgrading, which is only used for testing

## Slide 37: Backup / Restore User data
System Administration -> Backup-Restore tab allows user to backup and then restore user data:
  Node-RED flows
  Grafana dashboards
  Movicon projects
  Timescale and InfluxDB databases
Each back up is encrypted and password protected
Note that when restoring from the backup PACEdge device shall have same application and services passwords as when backup has been done. Otherwise, data in the databases can not be accessed.

## Slide 38: Licensing
System Administration -> Licensing tab allows user to view and manage PACEdge licenses.
Starting with PACEdge v3.0.0 Thales licensing tools have been implemented.
PACEdge devices come with the license installed and activated from the factory
In case of the Factory Image recovery, new license will have to be generated:
  Click on Generate Fingerprint and save file to local PC
  Email fingerprint file as well as serial number and device partnumber to support
  Install received license file

## Slide 39: Group Management
Group Management functionality:
  Update Linux OS
  Update PACEdge applications and services
  Update Node-RED flows
  Update Grafana dashboards
  Manage activated services and credentials
Ability to split devices into groups
Group Manager available on IPC6010/8010 as well as Virtual Machine, managing:
  10 Devices
  50 Devices
  100 Devices
  more devices on request
PACEdge Site
(Pipeline North)
PACEdge
Group Manager
Customer Intra-Net
Customer Plant
PACEdge Site
(Pipeline South)
PACEdge Site
(Plant Alpha)

## Slide 40: Group Management
System Administration -> Group Management tab enables user to setup device groups, where is the Update Groups tab enables user to perform updates
To take advantage of the Group Manager functionality, only the device designated as Group Manager needs to have a Group Manager license.
Note: once device is configured to be part of the group, Group Manager takes ownership of enabling/disabling services and setting user passwords.
Group Manager needs to have access to the Internet so that software updates can be downloaded. Managed devices only have to have connectivity to the Group Manager, but not to the Internet.
For more details on using Group Manager refer to the User Manual and dedicated examples and articles

## Slide 41: Factory Image Restore
PACEdge platform comes with utilities that allow users to restore software back to Factory Default image, which is useful when trying to recover from a catastrophic failure
Factory Default recovery procedure depends on the HW type:
  CPE400/CPL410 has a built-in recovery image, which can be activated via on-unit display and buttons
  IPC2010 requires an image to be downloaded from Emerson software download site and copied to the USB stick. A RS232 serial cable needs to be used so that user interface can be shown and user options selected.
  IPC6010/7010/8010 requires an image to be downloaded from Emerson software download site and copied to the USB stick. Monitor and keyboard needs to be attached directly to the unit so that user interface can be shown and user options selected.
Same software utility, placed on USB stick, can also be used to create a fully copy of the PACEdge installation, along with Linux OS, applications, utilities and their configuration. This backup image can then be used to either recover unit to the previous known state or prepare other hardware units with the exact same configuration

## Slide 42: PACEdge Upgrade from Older Versions to v3.0.0
PACEdge v3.0.0 is a significant change from the older PACEdge version
Due to Linux OS upgrade from 20.04 to 24.04, changes in how applications and services are being controlled, a whole new GUI layer a gradual upgrade of the PACEdge is not possible.
Upgrade procedure will require following steps:
  Using native Node-RED, Grafana utilities export flows to the local PC
  Copy InfluxDB and Timescale databases to the local PC
  Download software image from Emerson software center and copy it onto the USB stick
  Boot from the USB stick and select new installation option
  Generate HW fingerprint and email it to Emerson support
  Install license received from Emerson support
  Import back Node-RED and Grafana flows and dashboards, deploy Movicon projects